## Slide 1: 논문 요약 – PART 1

## Slide 2: Introduction
“We are on the cusp of revolutionary changes in communication and microsystems technology”
through the marriage of photonics and electronics on a single platform.

## Slide 3: Introduction
Electronic-photonic
circuits
Will play a ubiquitous role globally
High-speed communications
Ex) High-performance computing
medical applications
data centers

## Slide 4: Introduction
Electronic-photonics circuits
Every attempts to directly integrate photonic functionally into CMOS or bipolar silicon has yielded poorly-performing devices
Can we reused electronic industry`s capabilities?
Using the tools for truly advanced microelectronics to try to build photonics is a mistake

## Slide 5: Introduction
Silicon
Fantastic material system for building photonic devices as well as electronic ones!
Re-use is possible!
Silicon
Photonics

## Slide 6: Technical challenges
Waveguides and passive components
SOI wafers
Reduce the losses
Cost effective

## Slide 7: Technical challenges
Modulators
Plasma Dispersion Effect
MZI used
Significantly cost
High thermal sensitivity
Carrier-depletion mode device,
Based on a Reverse-biased pn junction

## Slide 8: Technical challenges
Photodetectors, Light sources ..

## Slide 9: Modelling and design approaches
Passive Optical
Active Optical
Electrical
Component Models
About silicon photonics!

## Slide 10: Optical waveguide mode solver
Waveguide mode
Transverse field
Do not change shape
Time-invariant

## Slide 11: Optical waveguide mode solver
What is an eigenmode?
Boundary condition에 따라 결정되는 전자기파의 해
Mode?
파면의 형태

## Slide 12: Optical waveguide mode solver
Eigenmode Solvers
Determine time-harmonic solutions to Maxwell`s equations in the frequency domain
Numerous simulations are required to obtain wavelength sweeps needed to study waveguide dispersion
FEM, FD, EIM

## Slide 13: Optical waveguide mode solver
FEM – Finite Element Method
Particularly well suited for high-index contrast structures
Has the benefit that the mesh is compatible with the finite difference time domain(FDTD)
FD – Finite Difference
Mesh is unstructured(Flexible meshing is desirable)
Useful for three-dimensional structures

## Slide 14: Optical waveguide mode solver

## Slide 15: The simulation steps
Define waveguide structure including the waveguide and the cladding
Specify the materials
Choose a mesh and accuracy
Choose boundary conditions
Specify the wavelength, or range of wavelengths

## Slide 16: Wave propagation
FDTD
“The design of photonic devices usually requires an understanding of how light will propagate in the structure”
Non-uniform devices
Reflections
Interference
Scattering
Radiation

## Slide 17: Wave propagation- 3D FDTD
FDTD
Numerical method for solving the 3D Maxwell equations (exact)
Useful for analyzing the interaction of light with complicated structures
Simulates the propagation of a pulse of light which contains a broad spectrum
A single simulation provides the response of the optical system for a wide range of wavelengths at once
Can model materials that are dispersive and nonlinear (of course LTI too)
Computationally intensive

## Slide 18: Wave propagation- 3D FDTD

## Slide 19: Wave propagation- 2D, 2.5D FDTD
2D FDTD
Faster than 3D
Invariant 한 part -> 2D, 아닌거 3D
2.5D FDTD
Dramatically improving speed
The structure is invariant in one dimension

## Slide 20: Wave propagation- Other Method
BPM – Beam Propagation Method
EME – Eigenmode Expansion Method
An approximate solution, ‘exact’ solution of Maxwell`s equations
For structures with small index of refraction contrasts, typically as a scalar solution
Useful for designing Mach-Zehnder interferometers
Considered the propagation of light by decomposing
Accurate for an infinite numbers of modes

## Slide 21: Wave propagation- Other Method
CMT – Coupled Mode Theory
TMM – Transfer Matrix Method
Widely used for solving optical structures such as couplers
Based on perturbation
Very simple and fast technique
For refraction profile
Provides an exact answer for one-dimensional structures such as TF reflectors

## Slide 22: Modellings